Requirements
- If your robot about to crash or drive off an edge, it must stop immediately
  For this you need IR sensors all around the the body, and ideally, underneath as well.
- In order to keep the robot from veering left or right, you need to know how far each wheel has traveled
  For this you need at least two disc encoders with optical sensors
- As your project progresses, you’ll want to add more features.
  For less than 8$, you can get a box with 37 sensors, most of which could be useful, or at least fun to add.
  Buzzers, Movement detectors (are the wheels spinning?), relays, color detectors (for line following and more), tilt switches, temperature sensors, sound detectors, shock detectors, humidity detectors (we don’t want to get wet!)
  Combining multiple input types, you can make inferences about the state of the robot and its environment.
  The more capabilities you add, the more awesome your robot becomes
- However ...

---
Limitations
- … the ESP32 has 36 IO pins
  This may seem like a lot at first, but as you add sensors, distance measuring, GPS, … you’ll find the number of free pins dwindeling faster than the money in an average pensioner’s bank account
- In order to connect all your devices to the ESP32, you will have to make some kind of mainboard anyway, so why not solve two problems at once?

---
ESP32 Superexpander
The ESP32 Superexpander gives you
3 headers for VL53L0X laser distance meters
4 I²C headers
2 headers for wheel motion IR sensors
1 header for L298 or compatible motor driver
12 on-off outputs for relays, switches, …
8 on-off inputs for sensors
12 breakouts for GPIO pins

---
Counters
- For some input, we need to know immediately if it goes active, e.g. an imminent crash or other catastrophe. An Interrupt Service Routine must set a variable and disable the motor before returning.
- For other inputs, like wheel motion, it’s enough to know how far we’ve traveled on each iteration. However, wheel motion arrives in tiny millimeter increments, and when driving at full speed, they arrive too fast for us to poll them. We need one interrupt handler for the left wheel and one for the right, updating two variables that we can read on each iteration.
  With all the other stuff that will be going on, reading a compass, reading lasers, communicating telemetry over UDP, avoiding obstacles, calculating trajectories, …. having two ISRs just for keeping track of wheel motion seems like an awful waste of resources.
- Why not offload the millimeter counting to a special purpose circuit like the 4060 and the read the count from a register on each iteration?

---
Design
Putting it all together in KiCad, you might get something like this

---
BLINKENLIGHTS!!!
… and, if you’re not careful when selecting resistor values for the LEDs, when you hook it up and turn on the power, it will look like this (which is what I wanted anyway because I’m crazy):

---
Outputs
Blink all outputs
Step through all 16 outputs, turning them on and off in sequence
: blinkoutputs
16 0 DO
i outputon writeboard
100 ms
i outputoff writeboard
100 ms
LOOP
;

---
Outputon
- The output number n must be on the stack
- If n is less than 8, set the nth bit in the value outreg1
- Else set the (8-n)th bit of outreg2
- Write the values of outreg1 and outreg2 to the board using writeS2P
: outputOn ( u -- )
   dup 8 < IF
    1 swap lshift outreg1 or to outreg1
  ELSE
    1 swap 8 - lshift outreg2 or to outreg2
  THEN
;

---
Gear_forward, Gear_backward
- Forward: Set bits 0 and 2, clear bits 1 and 3 in outreg1 without touching other bits
- Backward: Set bits 1 and 3, clear bits 0 and 2 in outreg1 without touching other bits
: gear_forward
  binary
  outreg1 10101111 and 10100000 or to outreg1
  decimal
;
: gear_backward
  binary
  outreg1 01011111 and 01010000 or to outreg1
  decimal
;

---
WriteS2P
- Stack contains the two registers to be written
- Clear the LATCH
- Write the first
- Write the second
- Set the LATCH bit
    S2P_LATCH 0 digitalWrite
    8 0 DO
        dup 1 and
        S2P_SCL 0 digitalWrite
        S2P_SDA swap digitalWrite
        S2P_SCL 1 digitalWrite
        1 RSHIFT
    LOOP
    Drop
    …
     S2P_LATCH 1 digitalWrite

---
Inputs
- 2 counters
- 8 binary inputs
- Use readP2S to read (leaves three numbers on the stack)

---
Showboard
Show the status of the inputs
NB: The inputs are inverted, 1 means 0 and 0 means 1.
Counter value = 255-value.
: showBoard
  readp2s
   ." Inputs " binary . cr
   ." Left wheel " decimal 255 swap - . cr
  ." Right wheel " 255 swap - . cr
;